## Slide 1
Energy-Oriented CGLA Mapping of a Memory-Polynomial Digital Predistortion Kernel
Takuto Ando and Yasuhiko Nakashima
Nara Institute of Science and Technology, 8916-5 Takayama-cho, Ikoma, Nara 630-0192, Japan.
Background & Objective
Digital Predistortion
・RF power amplifiers (PAs) introduce nonlinear distortion.
・Digital Predistortion (DPD) compensates for this distortion.
・Memory-polynomial DPD requires repeated complex arithmetic [1, 2].
Objective: Can a 15-term complex-MAC reduction be mapped onto CGLA's one-dimensional PE pipeline?
Map a 15-term DPD kernel onto the CGLA accelerator IMAX.
Evaluate its performance and energy efficiency.
CGLA Accelerator IMAX
CPU-Grounded Linear Array (CGLA) [3] Programmable ASIC architecture + VPK180 SoC (ARM CPU + FPGA)
Methods & Results
DPD Mapping on CGLA (like building an FPGA-style computation pipeline using programmable PE. )
• Synthetic check validates the 15-term correction form.
• Real PA and coefficient adaptation remain outside scope.
FPGA kernel-only latency 1.948 ms 28 nm projection 0.336 ms
Host preparation remains outside the mapped reduction.
Experimental Setup
Item | Setting
Workload | 32 × 2048 complex samples
Representative tile | 1024 samples
FPGA | 145 MHz, 64 PEs, 512 KB LMM
DPD form | (P, M) = (5, 5), 15 odd-order terms
Coefficient set | 120 B
Platform Results
Platform | Latency type | E2E latency | Energy / batch
RTX 4090 | Measured | 0.484 ms | 314.6 mJ*
Jetson AGX Orin | Measured | 4.478 ms | 67.2 mJ*
IMAX FPGA | Measured | 20.201 ms | N/A
IMAX 28 nm | Projected | 3.14 ms | 1.86 mJ*
* GPU 650 W × 0.484 ms. Jetson 15 W × 4.478 ms. IMAX 1.161 W × 0.336 ms + 0.525 W × 2.80 ms. Model-based energy, not measured runtime power.
Conclusion
・We successfully mapped a 15-term memory-polynomial DPD kernel onto a 33-stage IMAX pipeline, enabling streaming complex-MAC computation.
・The projected 28 nm IMAX achieved 169.1× lower modeled energy per batch than RTX 4090, although the GPU achieved lower end-to-end latency.
Future work will focus on integrating coefficient adaptation and continuous streaming toward practical real-time DPD processing.
[1] L. Ding et al., “A robust digital baseband predistorter constructed using memory polynomials,” IEEE Trans. Commun., vol. 52, no. 1, pp. 159–165, 2004.
[2] D. R. Morgan et al., “A generalized memory polynomial model for digital predistortion of RF power amplifiers,” IEEE Trans. Signal Process., vol. 54, no. 10, pp. 3852–3860, 2006.
[3] T. Akabe, V. T. D. Le, and Y. Nakashima, “IMAX: A power-efficient multilevel pipelined CGLA and applications,” IEEE Access, vol. 13, pp. 31899–31911, 2025.
APCCAS 2026
End-to-end latency (ms)
Chart: 
| FPGA · measured | IMAX · projected | RTX 4090 · measured | Jetson · measured
End-to-end latency (ms) | 20.201 | 3.14 | 0.484 | 4.478
Modeled energy ratio (IMAX = 1)
Chart: 
| IMAX | RTX 4090 | Jetson
Modeled energy ratio (IMAX = 1) | 1 | 169.1 | 36.1
ID: 2103
Selected References
* This work focuses on the hardware acceleration of memory-polynomial DPD, rather than the development of a new DPD algorithm. RF hardware measurements and adaptive coefficient updates are outside the scope of this study.
64-PE IMAX array. The 33 stages correspond to PE0 – PE32
used in this mapping PE0–PE32 (33 PEs)
unused by this mapping PE33–PE63
input pair
ordered stream
PE0
stream advance
PE1
history + coefficients
PE32
completed output
Output
packed result
15 terms = 5 delay taps × 3 odd orders (p=1,3,5) | PE0 advances the stream, PE1 supplies local state, PE2–PE31 reduce, and PE32 writes output.
PE2–PE3
term 0
term × coeff.
accumulate
PE4–PE5
term 1
term × coeff.
accumulate
PE6–PE27
terms 2–12
term × coeff.
accumulate
PE28–PE29
term 13
term × coeff.
accumulate
PE30–PE31
term 14
term × coeff.
accumulate
DPD digitally compensates for nonlinear distortion in RF power amplifiers (PAs).
We target a memory-polynomial computation kernel.
y[n] = ∑ ∑ aₚ,ₘ · x[n−m] |x[n−m]|ᵖ⁻¹ (m = 0,…,4, p ∈ {1,3,5})
Basis term
Coefficient
Coefficient : Fixed complex DPD coefficients.
All 15 coefficients remain in LMM for reuse during execution.
Basis term : Input transformed for order p and delay m, expanded on the host before transfer to IMAX.
2. PE0–PE1 Input preparation PE0 advances the per-pair basis offset.
PE1 issues term loads and supplies local state and coefficients.
3. PE2–PE31 Complex- MAC reduction Two PEs process each of the 15 terms.
Basis values are multiplied by coefficients and accumulated.
4. PE32 Output store PE32 stores the accumulated complex output.
The mapping uses 15 × 2 + 3 = 33 stages of the 64 - PE array.
1. Host preparation
The host expands 15 basis terms per sample.
Each 1024-sample tile contains 512 packed pairs.
Processing System
User Space
ARMv8
Cortex-A72
Kernel Space
LPDDR4
Low 4GB
High1 4GB
High2 4GB
Processing Element (PE)
Local Memory Module (LMM)
DMA Controller
#0
#1
#2
#3
#4
#5
#6
#7
IMAX 8 Lane
AXI DMA READ
AXI DMA WRITE
Network-on-Chip
(NoC)
CGLA Configuration
Notes: Source manuscript: cgla_research/papers/icecs_2026_dpd/main.tex and its included sections. Visual references: socc_poster.pptx and sasimi2025_poster.pptx in generated_20260728_takuto_style. A0 portrait, 84.1 × 118.9 cm, according to the supplied APCCAS poster instructions. Energy values follow the manuscript's phase-separated model, not the generic IMAX default. FPGA/RTX/Jetson latency measured, IMAX 28 nm projected; all energy numbers are modeled. Synthetic PA results are held-out waveform checks, not RF measurements. Editable text, tables, dataflow shapes and charts. Architecture is the manuscript image.
Revised from the author-selected green poster. A0 portrait 84.1 × 118.9 cm; Epapers ID 2103. Mapping labels are grounded in cgla_research/papers/icecs_2026_dpd/proposed.tex and main_ja.tex, including the seed, two-PE term, local coefficients, packed pairs and final-store boundary. Measured/projected values and all chart/table data are preserved.
Balanced layout 02_side_notes: original Fig. 2 is unchanged; green design, A0 and ID 2103 retained. All source table/chart values and non-mapping text retained.
Readability revision of the author-selected 02_side_notes. Original Fig.2 remains 56 cm wide, unchanged. Body, table, axis and data-label fonts enlarged; text boxes and margins adjusted without changing claims, chart data or table values. A0 portrait; Epapers ID 2103; source preserved.
Mapping side notes grouped into three quiet green cards. The packed-pair and term-count headings and basis formula have separate typographic emphasis. All original wording/data preserved.
Footer references added from existing main.bbl: ding2004memory, morgan2006gmp, imax_access. No external/new citations added. Previous footer qualifier: Measured: FPGA / RTX 4090 / Jetson AGX Orin | Projected: IMAX 28 nm | *Model-based platform energy